## Slide 1: Turbine as a Sensor Analytics
Mark Lynass
Scott Evans, Yunwen Xu
Sara Delport, Samuel Davoust
Murray Fisher

## Slide 2: Lubbock Analysis

## Slide 3: Power Estimation
Variability appears in traditional Power Curve estimation
Power difference
Explore the correlation between power deficit ~ shear
Power.diff = (ActualPower – FittedPower)

## Slide 4: Shear is a Factor
Shear is an important driver of power variation
    HHWS only is not sufficient to capture wind speed over vertical range
    Power ~ cubic law wrt wind speed
Shear is not commonly used in power estimation
Flat
Flatter than power law
PowerLaw
Normal shear
LowLevelJet (LLJ)
Larger curvature than power law

## Slide 5: Shear Characterization
PowerLaw
Shear exponent appropriately captures vertical wind speed gradient
LLJ
Shear exponent is not fully capture, need further characterization
Larger curvature than power law
Characterize as quadratic function

## Slide 6: LLJ Characterization - Quadratic Form
Formula
Fit one quadratic function to every 5-heights Wind Speeds
  are determined by minimizing Energy difference between fitted curve and measurements
  - area factors at 5 heights
Get summary statistics for all a and b

## Slide 7: Metamodel for Flex5 -- with Sara Delport, Samuel Davoust, and Murray Fisher

## Slide 8: DOE Planning - Wind Speed Interval Approach - Power Decomposition
f-term (main power curve): determined by HHWS Power (v) = mean ( power | if den.corr.HHWS in [v-0.5, v+0.5] )
g-term (residual of main PC): variation caused by other wind conditions
  Select data points centered at den.corr.HHWS [v-1, v+1]
  Analyze by conditional decision tree
Power = f(den.corr.HHWS) + g(a, b, veer, TI, density)
f(den.corr.HHWS)
Residual
WS window
[7,9]

## Slide 9: DOE Planning
DOE matrix
f-term
    HHWS = [4, 5, 6, 7, 7.5, 8, 8.5, 9, 9.5, 10, 11, 12]
  g-term
  Create a decision tree for power variation for data in each WS bin. Generate k input vectors (a, b, density, TI, veer) for each tree
  Joint distribution of (a, b)
  Sampling veer, density and TI on all terminal nodes
Total # DOE points = #(HHWS) * k
(a, b)
TI, veer, density
Power = f(den.corr.HHWS) + g(a, b, veer, TI, density)

## Slide 10: Sample (a, b) based on joint distribution
Sample density, veer and TI from marginal distribution

## Slide 11: Neural Network to Reconstruct Power Estimation Relationship in FLEX5
Intelligent Sampling

## Slide 12: NN Performance on Field Data

## Slide 13: Final Shear Estimation Pitch

## Slide 14: Shear Estimation from Turbine Sensors
Scott Evans, Yunwen Xu, Sara Delport
Mark Lynass

## Slide 15: Outlines
Observation based on Lubbock 5 speed metmast
    Shear type is a driver of power variability
Analysis performed using onboard turbine sensors (e.g. loads)
    Shear inference
    Opportunities in AEP optimization, lifing, Farm Controls….

## Slide 16: Observation from Lubbock Metmast Analysis
Shear Types
Power differential driven by Shear Type
  Low-level-jet ~~ under production
  Flat ~~ over production
Type | Power law | Low-level-jet | flat | other
Portion | 79% | 14.5% | 4.5% | 2%
Flat
Flatter than power law
PowerLaw
Normal shear
LowLevelJet (LLJ)
Larger curvature than power law
Power difference

## Slide 17: Classification Formulation
  Motivation
    Shear profile is a main driver for power performance
    Every two classes are statistically different (except power law vs. other)
    Can we identify the classes (especially LLJ) from load sensor signals?
Statement and objective
    Use load sensors signal to predict wind shear profiles
X
Nodd
Pitch
Yaw
RPM
P_el
MBC V_estim
Y
(Class label)
PowerLaw
LLJ
Flat
    Low Level Jet < Power Law < Flat
After Classified, We will infer Shear Parameter(s)

## Slide 18: Shear Estimation Process
Inputs
ML algorithm

## Slide 19: Input Signal from Load Sensors
2 min averaged signal
X: Available from load sensors
Turbine sensor signal used to classify Shear Type and Infer Shear Parameters
Variable importance
Most important Features are nodding 3C and Yaw 3C Components

## Slide 20: Shear Estimation - Random Forest
Shear Type Classification Result

## Slide 21: Performance Summary - Random Forest
Shear Type classification
Confusion matrix
Overall accuracy = 91.9%
Alpha estimation
A estimation
B estimation
7.5% misclassification
MAE = 0.031
MAE = 3.2e-4
MAE = 7.2e-6
0: Power Law
1: Low Level Jet
2: Other
3: Flat

## Slide 22: Shear Estimation in Streaming